## Slide 1
MIZU
(Monitoring of Irrigation Zones Using satellites & IoT)
Phanish
Ojas
Shohei
Joseph
Debrupa
Yuzuki
Supporters

## Slide 2
1. User Needs/Background
Proper water resource management is essential for agriculture.
➢ For example, rice irrigation in dry season is a challenge in Kenya and Tanzania.
Proposed solution steps:
1. Rainfall prediction from weather data using IoT sensor
2. Soil moisture monitoring using IoT sensor
3. Irrigation optimization
Most of Kenyan land is semi-arid
Rice irrigation in Tanzania

## Slide 3
1. User Needs/Background
IoT sensor data
Temperature, humidity, wind,
solar radiation, soil moisture, soil temperature, rain gauge*, surface moisture*, leaf wetness*
Satellite rainfall data
(IMERG, CHIRPS)
Precise
evapotranspiration
Precise rain fall prediction
Precipitation Forecasting with Data Assimilation (Ensemble Kalman Filter)
Irrigation optimization
Constrained Model Predictive Control
Objective
function
Constraints
SWAT model
(Hydrology
model)
IoT & Satellite can be used for optimal water irrigation

## Slide 4
[MG-1] Uplink the weather and agricultural data from IoT sensors to satellites
[MG-2] Downlink the stored data from satellites to ground stations
2. Mission Goal/Objective
Concept sketch
IoT sensors
(network unavailable areas)
Ground station
End users (farmers)
Satellite

## Slide 5
Success Level | No. | Mission Success Criteria | Verification Method
Minimum Success | [MG-1] | Acquire data from various sensors | Acquired data from the sensors is displayed on the terminal
 | [MG-2] | Aggregate the sensor data and transmit them to the Satellite | Transmitted data is displayed on the terminal connected to the HEPTASAT
Full Success | [MG-1] | Received aggregated data transmitted to the ground station | Aggregated data displayed on the Ground Station Terminal
Advanced Success | [MG-2] | The ground station decompose the aggregated data and display the results on the ground station interface | Various sensor data is displayed on the Ground Station interface
Advanced Success | [MG-1] | Aggregate data from multiple sensor nodes and uplink the data to the satellite | Decompose data from multiple sensors and display on the HEPTASAT Terminal
 | [MG-2] | Relay the aggregated data to the second HEPTASAT to form a constellation of satellites | Receive the data from HEPTASTA1 to HEPTASAT2
3. Success Criteria
[MG-1] Uplink the weather and agricultural data from IoT sensors to satellites
[MG-2] Downlink the stored data from satellites to ground stations

## Slide 6
4. Mission Sequence
Sensors
Ground station
Satellite

## Slide 7
5. Block Diagram

## Slide 8
6. Components
No.​ | Components​ | Model Number​ & URL​ | Where to get​ | Qty​ | Unit Price​ (Tax 10%)​ | Total​
1​ | Temperature and Humidity Sensor | ST0248 | Provided | 2 | 0 | 0
2​ | Wind Speed Sensor |  | Provided | 2 | 0 | 0
3 | Solar Radiation Sensor 1 (Ambient light sensor) | TEMT6000 | Provided | 2 | 0 | 0
4 | Solar Radiation Sensor 2 (UV sensor) | Grove-UV | Provided | 2 | 0 | 0
5 | Soil Moisture | SEN0114 | Akizuki | 2 | 550 | 1100
6 | Soil Temperature sensor (Hepta-sat temp. sensor) |  | Provided | 2 | 0 | 0
7 | GPS sensor |  | Provided | 2 | 0 | 0
8 | Mbed Board | LPC1768 | Provided | 2 | 0 | 0
​ | Total (JPY)​ | ​ | ​ | ​ | ​ | 1,100

## Slide 9
7. Schedule Management Result
Action Item | Person in charge | Day 1 |  |  |  | Day 2 |  |  | 
 |  | 9 | 12 | 15 | 18 | 9 | 12 | 15 | 18
Sensor Verification | Phanis/Ojas |  |  |  |  |  |  |  | 
development of GS | Joseph |  |  |  |  |  |  |  | 
System integration and verification Satellite System | Shohei |  |  |  |  |  |  |  | 
Prepare final presentation | All |  |  |  |  |  |  |  |